IT ESSENTIALS V. 4.1

Module 3

Computer Assembly Step-by-Step

| 3.1 Open the Case |
| --- |
| 1. | What does form factor refer to? | Size and shape of the case |
| 2. | How should the workspace be prepared? | Adequate lighting, good ventilation, comfortable room temperature, workbench accessible from all sides |
| 3.2 Install the power supply |
| 3. | What are the power supply installation steps? | Insert power supply into case Align holes in power supply with holes in case Secure power supply to case using proper screws |
| Virtual Desktop |
| Lab: Install Power Supply |
| 3.3 Attach the components to the motherboard and install the motherboard |
| 3.3.1 Install a CPU and a heat sink/fan assembly |
| 4. | How is the CPU secured to the socket on the motherboard? | With a locking assembly |
| 5. | What is thermal compound used for? | To help conduct heat away from the CPU |
| 6. | How do you clean a used CPU? | Isopropyl alcohol |
| 7. | What is the heat sink/fan assembly? | A two-part cooling device |
| 8. | What is the connection 1 indicator on the CPU lined up with on the CPU socket? | Pin 1 |
| 3.3.2 Install the RAM |
| 9. | What does RAM provide? | Temporary data storage for the CPU while the computer is operating |
| 10. | What is meant by volatile memory? | Its contents are lost when the computer is shut down |
| 3.3.3 Install the motherboard |
| 11. | What is used to mount the motherboard and to prevent it from touching he metal portions of the case? | Plastic and metal standoffs |
| Virtual Desktop |
| Lab: Install the Motherboard |
| 3.4 Install Internal Drives |
| 12. | What are the steps for installing a hard disk drive? | Position the HDD so it aligns with the 3.5 inch drive bay Insert the HDD in drive bay so screw hold in drive line up with screw holes in the case Secure the HDD to case using proper screws |
| Virtual Desktop |
| 3.5 Install drives in external bays |
| 13. | What are external bays? | Allow access to the media without opening the case |
| 3.5.1 Install the optical drive |
| 14. | What is an optical drive? | A storage device that reads and writes information to CDs and DVDs |
| 15. | What kind of connector provides power to the optical drive from the power supply? | Molex |
| 16. | What kind of cable connects the optical drive to the motherboard? | PATA |
| 3.5.2 Install the Floppy Drive |
| 17. | What is a floppy disk drive (FDD)? | A storage device that reads and writes information to a floppy disk |
| 18. | What kind of power connector provides the FDD with power from the power supply? | berg |
| Virtual Desktop |
| Lab: Install the Drives |
| 3.6 Install adapter cards |
| 19. | Why would you use adapter cards? | To add functionality |
| 3.6.1 Install the NIC |
| 20. | Why do you need a NIC? | To connect to a network |
| 3.6.2 Install the wireless NIC |
| 21. | What type of expansion slots do wireless NICs use? | PC I & PCIe |
| 3.6.3 Install the video adapter card |
| 22. | What is a video adapter card? | The interface between a computer and a display monitor |
| 23. | What type of expansion slots do video adapter cards use? | PCI, AGP, PCIe |
| Virtual Desktop |
| Lab: Install Adapter Cards |
| 3.7 Connect All Internal Cables |
| 24. | What are power cables used for? | To distribute electricity from the power supply to the motherboard and other components |
| 25. | What do data cables do? | Transmit data between the motherboard and storage devices |
| 3.7.1 Connect the power cables |
| 26. | Haw many pins does the ATX main power connector have? | 20 or 24 |
| 27. | How many pins are on a SATA power connector? | 15 |
| 28. | What is a 4-pin berg connector used for? | Floppy drive |
| 3.7.2 Connect the data cable |
| 29. | What are the types of data cables? | PATA, SATA, floppy drive |
| 30. | What is another name for a PATA cable? | Ribbon cable |
| 31. | What does a stripe on the data cable indicate? | Location of pin 1 |
| 32. | Where is the pin 1 indicator on the drive connector? | Closest to the power connector on the drive |
| 33. | If a motherboard has two PATA drive controllers, how many PATA drive can it support? | 4 |
| 34. | What type of connector does a SATA data cable have? | 7 pin |
| 35. | What type of a connector does a floppy drive data cable have? | 34 pin |
| 36. | If the floppy drive activity light displays continuously, what is the problem? | Ribbon cable is not installed correctly |
| Virtual Desktop |
| Lab: Install Internal Cables |
| 3.8 Reattach the side panels and connect external cables to the computer |
| 3.8.1 Re-attach the side panels |
| 3.8.2 Connect external cables to the computer |
| 37. | Should you force a connector? | No |
| 38. | When should you plug in the power cable? | After you have connected all other cables |
| Virtual Desktop |
| Lab: Complete Computer Activity |
| 3.9 Boot the computer for the first time |
| 39. | When booting a computer, what performs a check on all of the internal components? | BIOS –basic input/output system |
| 40. | What does POST stand for? | Power-on Self-Test |
| 3.9.1 Identify Beep Codes |
| 41. | What does POST check for? | To see that all of the hardware in the computer is operating correctly |
| 42. | What does a single beep indicate? | The computer is functioning properly |
| 43. | What determines what the beep codes mean? | The BIOS manufacturer |
| 3.9.2 Describe BIOS setup |
| 44. | What is contained in BIOS? | Setup programs used to configure settings for hardware devices |
| 45. | What does CMOS stand for? | Complementary Metal Oxide Semiconductor |
| 46. | What key is typically pressed to enter the BIOS setup program? | DEL |
| LAB: Boot the Computer |