## Slide 1
Basic Procedures for Shop Safety
• Adhere to instructions from the following sources:
 Labels and warnings on containers and tools
 The manufacturer’s recommendations for use and maintenance of specific tools
 Signs posted in the work area
 Directions given by the instructor
• Wear safety glasses in the shop at all times.
• Wear protective gear such as gloves, earplugs, and safety shoes if appropriate.
• Do not wear loose-fitting clothing that could get caught in a moving part.

## Slide 2
Basic Procedures for Shop Safety
(Continued)
• Secure long hair to avoid getting it caught.
• Keep work areas clean and free of clutter.
• Inspect each tool before using it to make sure it is working properly.
• Tell the instructor about any damaged tool.
• Do not use a tool that does not function properly.
• Return each tool to its proper place of storage.

## Slide 3
Portable Drill

## Slide 4
Circular Saw
Note that the teeth turn up toward the cut.

## Slide 5
The blade should be at full speed before cutting begins.

## Slide 6
Reciprocating Saw
The shoe of the reciprocating saw is adjustable. It should be kept firmly against the work at all times.

## Slide 7
Band Saw
Before using a band saw, plan the cuts and be sure the stock will clear the arm of the saw.

## Slide 8
Table Saw

## Slide 9
Use of a Push Stick
With a Table Saw
Use a push stick to guide smaller stock.

## Slide 10
Shaper
Shapers are used for forming edges and cutting dados and other joints.

## Slide 11
Jointer
The outfeed table should be set at the same height as the top of the cutting blade to avoid tapering or binding the stock.