## Slide 1
Sample Cutting List and Bill of Materials
Bluebird House
Cutting list:
1 - 16 ½" x 1" x 6" pine board – back
1 - 9 ¾" x 1“ x 6" pine board – front
1 - 6 ½" x 1" x 6" pine board – roof
2 - 10 ¾" x 1" x 6" pine boards (ripped to 4") – sides
1 - 4" x 1" x 6" pine board (ripped to 4") – bottom
1 - 5 ½" x ¾" x ¾" pine board – roof holder
Purchasing bill of materials:
1 - 5' x 1" x 6" pine board
20 - 6p (six-penny) finish nails
1 - 1 ½" screw
Part Name | # of Pieces | Size Thick | Width | Length | Type of Material | Price/Unit | Price/Ft | Cost
Board | 1 | 1" | 6" | 5' | Pine board |  | $0.25 | $1.25
Six-penny nails | 20 |  |  | 6d | Finish nails | $0.01 |  | $0.20
Screw | 1 |  |  | 1 1/2" | Screw | $0.02 |  | $0.02
Total Cost |  |  |  |  |  |  |  | $1.47