## Slide 1: Poplar Bluff Technical Career Center Graphic Communications
Shop Safety
Notes: <number>

## Slide 2: Shop Safety
In this unit you will:
Learn vocabulary terms
Learn shop safety rules
Learn steps in maintaining safety and order in the shop
Learn listed information on a Material Safety Data Sheet
Learn the steps to take in case of an emergency
Notes: <number>

## Slide 3: Vocabulary Terms
Solvents
Combustibles
Personal Protective Equipment
Hazard
Material Data Safety Sheet (MSDS)‏
Occupational Safety and Health Administration (OSHA)‏
Ergonomics
Lockout Device
Machine Guards
  The definitions to these terms are provided in your in your information sheet handout.
Notes: <number>

## Slide 4: Shop Safety Rules
In order to have a safe shop you must abide by the shop safety rules listed below:
Conduct yourself in a manner conducive to safe shop practices.
Do not use any equipment until you understand how to use it.
Operate any presses or electrically powered equipment only after obtaining the approval of your instructor.
Never walk away from equipment that is running.
Always keep your hands away from a machine’s moving parts.
Use the correct tools and equipment when doing a job.
Limit the operation of the paper cutter, paper drill, and stitcher to one person at a time.
Tie back all long hair prior to operating any press or power equipment.
Notes: <number>

## Slide 5: Shop Safety Rules Continued...
Remove ties, scarves, loose clothing, rings, and other jewelry before operating any press or power equipment.
Do not sit or lean on light tables.
Avoid touching or looking directly at light sources.
Wear eye protection in areas where flying objects and splashing solutions are possible.
Do not touch heat sources with hands or other body parts.
Wear hearing protection when subjected to continuous loud noise.
Wash hands and arms with soap and water frequently to help prevent skin irritation from inks and solvents.
Do not engage in horseplay, scuffling, or practical joking in the classroom or shop.
Use the “buddy system” when working in the graphics laboratory.
Notes: <number>

## Slide 6: Maintaining Safety and order in the shop
In order to maintain safety and order in the shop you must abide by the following guidelines listed below.
Report any unsafe condition in the shop immediately.
Arrange all machinery and equipment to permit safe and efficient operation.
Keep materials and supplies safely stacked and stored.
Keep all tools and accessories in cabinets, drawers or tool racks.
Dispose of or store all combustible material in safe containers.
Keep all floors clean and free of debris at all time.
Check that adequate housekeeping equipment and cleaning materials are on hand to ensure that maximum cleaning efficiency can be maintained.
Participate in daily cleanup periods.
Notes: <number>

## Slide 7: Machine Guards
Machine Guards protect body parts from being electrocuted, cut, squashed, or hit by flying fragments, that happen with equipment hazards
Equipment hazards:
  Spinning Rollers
  Rotating chains & sprockets
  Turning Gears
  Rotating Belts

## Slide 8: Machine Hazards
Machine Hazards

## Slide 9: Tag out
Tagout device – a prominent warning, such as a tag fastened to a machine.
Use a “tagout” tag if a machine is broken.

## Slide 10: Safe Lifting
Make sure you have a clear path for carrying things
Check object’s weight
Request help
Keep back straight
Lift with your knees
Keep objects close to body
Tighten stomach
Put things on floor carefully

## Slide 11: Fire Prevention
Combustable = Flamable
Solvent – chemical that disolves other substance
To prevent fire –
  Never sit solvent soaked rags on heat sources
  Report leaking solvent containers
  Put rags in fire safe container

## Slide 12: Material Safety Data Sheet
When working with chemicals you need to know certain things about chemicals when emergencies come up.
Below you will find types of information found on a material safety data sheet. All chemical products have this information available upon request if it is not shipped with your order.
Chemical name
Hazardous ingredients/chemical identity.
Physical characteristics
Fire and explosion data
Reactivity
Health hazards
Usage, handling, and storage
Special protection and precautions
Notes: <number>

## Slide 13: Ergonomics
In order to avoid back, neck, and knee injuries, and carpal tunnel syndrome, be sure to watch your posture at your desk:
Sit and work at computer with:
thighs horizontal
lower legs vertical
feet flat on floor
wrists flat
monitor not too close or far away from face – your neck should be straight.
Notes: <number>

## Slide 14: Emergency
Here are the proper steps to take in case of an emergency:
1. Turn off power if power is involved
2. Report to instructor
3. Administer first aid, if qualified and possible
4. If chemicals are involved fill out MSDS sheet
5. Report to administrator
6. Call nurse or take injured person to nurse
7. Notify parents
8. Instructor fill out necessary accident forms.
Notes: <number>

## Slide 15: Credits:
References:
Texas Trade & Industrial Education website
Book – Graphic Communications
Instructor – Regina Gossett, Poplar Bluff Technical Career Center
Notes: <number>