## Slide 1: Safety Press Procedures
New Madrid County Central
Technical Skills Center
Graphic Arts

## Slide 2: Offset Lithography
Printing method in which inked images are offset or transferred from one surface to another.
Printing presses can introduce an abundance of potential safety hazards.
Always be aware of personal safety, shop conditions and mechanical safety.

## Slide 3: Personal Safety
Roll shirt sleeves up to elbows
Tie back long hair
Remove all jewelry
Do not carry wiping cloths in pocket
Wear eye protection when needed
Be aware of your surroundings
No horseplay around machinery

## Slide 4: Shop Conditions
Aprons should be hung out of the way
Floors/aisles should be free of debris/oil/grease
Solvents stored in proper containers
Appropriate waste containers for paper, shop rags
Tools stored in toolbox
Oil drip pans emptied periodically
Paper/envelopes properly stacked/stored off of floor

## Slide 5: Mechanical Safety
Never operate any press until you have been instructed in its safe operation.
Pay close attention to mechanisms found on press such as spinning rollers, rotating chains, turning gears and rotating belts
Prepare inking unit after checking for lint/dust
Prepare dampening unit with the proper mixture of fountain solution
Attach plate paying close attention to the tension clamps
Set paper stock up while setting feeding tray at appropriate level
Check that all guards are in place before starting press
Stop press to clear all jams, make adjustments/repairs or to clean
After delivery of completed job, follow proper steps for cleaning and care of machine
Make sure solvents are used in well-ventilated areas
Wear eye protection
Dispose of ink and solvent covered rags in safe containers